## Slide 1
National Central University
Network Computing Laboratory, CSEE, NCU
Install Raspbian on Raspberry Pi 3 model B+

## Slide 2: Outline
Introduction
Build up system
Enable UART serial
Configure network
Connect to Pi (SSH)
Copy files to Pi (SCP, FileZilla)
2

## Slide 3: Introduction
Raspberry Pi 3 model B
3
From https://en.wikipedia.org/wiki/Raspberry_Pi

## Slide 4: Introduction
Raspberry Pi 3 model B
USB Port * 4
Ethernet
HDMI
Camera interface (CSI)
micro USB power supply (2A, 5V)
Micro SD cad slot (on the back of Pi)
40 GPIO Pins
Power-over-Ethernet

## Slide 5
Introduction
General-purpose input/output (GPIO)
Note that the physical PIN number is different from the GPIO number.

## Slide 6: Build up a system
Now, let we set up our Raspberry Pi system.
First, we need to download a Raspberry Pi operating system image file.
Then, we need to write that image to a SD card.

## Slide 7: Build up a system
Download OS
Download
https://www.raspberrypi.org/downloads/

## Slide 8: Build up a system
Download OS

## Slide 9: Build up a system
Writing an image to the SD card
1. Formatting SD card. (SD formatter)
https://www.sdcard.org/downloads/index.html
2. Writing an image to the SD card. (Etcher)
https://etcher.io/

## Slide 10: Build up a system
Formatting SD card
10
Step2. Select your SD card
Step3. Format the SD card
Step1. Choose OS
https://www.sdcard.org/downloads/index. html

## Slide 11: Build up a system
Writing an image to a SD card
To write an image to a SD card, the easy way is using Etcher which works on Mac OS, Linux and Windows. (May take long time to write the image)
11
Visit etcher.io and download and install it.
https://etcher.io/

## Slide 12: Build up a system
Writing an image to a SD card
Open Etcher and follow these 3 steps
1
2
3

## Slide 13: What's next ?
As we eject the SD card after Raspbian has been installed in it, we should consider how to operate Pi as Pi might not connect to Internet.
Have a monitor with HDMI cable, a USB keyboard and mouse.
Operate Pi directly and have fun.
Use UART to connect (TTL serial)
SSH connection with
Internet (IP needed)
VNC connection with Internet (IP needed)
Yes
No

## Slide 14: Enable UART
At the first time, your Raspberry pi has no Internet connectivity and doesn't enable SSH.
So, we have to turn on the UART port (TTL serial) to connect our Pi and then configure network settings and enable SSH.
PL2303HXD USB to TTL
We will use this PL2303HXD cable in this tutorial.

## Slide 15: Before the next step
As we need to modify some files in the SD card, we recommend to use Notepad++ or other editor to modify files because the default Notepad of Windows might have encoding issues with that file.
  Notepad++
https://notepad-plus-plus.org/
Don't forget to inject your SD card into your computer again.

## Slide 16: Before the next step
If you are using Windows, you will need Putty to connect your Pi by UART/TTL serial.
Download and install Putty.
https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html

## Slide 17: Enable UART
Step 1
Append the following lines to /boot/config.txt
dtoverlay=pi3-miniuart-bt core_freq=250 enable_uart=1

## Slide 18: Enable UART
Step 2
Delete "quiet" in /boot/cmdline.txt
Remove it

## Slide 19: Enable UART
After we have modified /boot/config.txt and
/boot/cmdline.txt in the SD card, we can eject the SD card from our computer and inject it into a Raspberry Pi.

## Slide 20: Enable UART
Step 3
20
Let Pi connect to TTL-to-USB cable as follows
Pin6: black line Pin8: white line Pin10: green line

## Slide 21: Enable UART
Step 4
Download PL2303 drive and install it
Windows:
  http://www.prolific.com.tw/US/ShowProduct.as px?p_id=225&pcid=41
  If your OS is Windows10, you can forward to next step to check that whether your computer could find COM port or not.
Mac OS:
  http://www.prolific.com.tw/US/ShowProduct.as px?p_id=229&pcid=41

## Slide 22: Enable UART
Step 5
As PL2303 drive is installed, we should turn on Raspberry Pi and connect it to our computer by USB to TTL cable.
Then, checking that our computer could find the USB to TTL cable.
The different OS systems have different ways for checking, thus the following are for
Windows and Mac OS .
Click here for Mac OS

## Slide 23: Enable UART
Step 6 (for Windows)
Open Device Manager and make sure that PORTs(COM & LPT) has USB-to-Serial Comm Port (COM x)
We will use that port to connect to Pi.

## Slide 24: Enable UART
Step 7 (for Windows)
Then, open Putty
24
1
2
3
4
5
The number you see in USB-to-Serial Comm Port (COM x)
Set Speed as 115200

## Slide 25: Enable UART
Step 8 (for Windows)
If we connect to Pi successfully, we could type username and password
Default setting username: pi password: raspberry

## Slide 26: Enable UART
Step 6 (for Mac OS)
Open the terminal and type:
ls /dev/cu*
If /dev/cu.usbserial appears, we can connect to pi by screen
screen /dev/cu.usbserial 115200
Screen user's manual
  https://www.gnu.org/software/screen/manual/ screen.html

## Slide 27: Enable UART
Step 6 (for Mac OS)
Default setting username: pi password: raspberry

## Slide 28: Common commands in Linux terminal
28
Commands:
ls: list files in this directory
cd: change directory to other directory
e.g., cd home/pi/test
cd ..: change directory to the upper directory
cd ~: change directory to home/pi sudo shutdown: shutdown the system
e.g., sudo shutdown –h now : shutdown the system immediately
sudo reboot: restart the system
Useful tips:
Press "↑": show the last command Press "Tab": auto complete

## Slide 29: Configure network
After we connect to our Pi by UART, we can configure the network settings of Pi.
Now, let we configure the WiFi settings.
  Before configure the WiFi, we should check our device has WiFi Interface wlan0, type:
ifconfig

## Slide 30: Configure WiFi
We can configure WiFi by these 2 ways
  raspi-config
  Modify wpa-supplicant configuration file
The following introduces how to configure WiFi by raspi-config.
  Type:
sudo raspi-config

## Slide 31: Configure WiFi
Step 1
Select 2 Network Options

## Slide 32: Configure WiFi
Step 2
Select N2 Wi-fi

## Slide 33: Configure WiFi
Step 3
Select the country

## Slide 34: Configure WiFi
Step 4
Enter your WiFi AP's SSID

## Slide 35: Configure WiFi
Step 5
Enter passphrase of that SSID

## Slide 36: Configure WiFi
Step 6
Verify whether your Pi has successfully connected.
Type
If inet addr field has no address, check that your password and SSID are correct by looking
/etc/wpa_supplicant/wpa_supplicant.conf
ifconfig wlan0

## Slide 37: Configure WiFi
Step 7
Type
sudo nano /etc/wpa_supplicant/wpa_supplicant.conf
Check the following two fields are correct. If not, modify them and reboot Pi
network={
ssid="SSID of AP" psk="password"
…
}

## Slide 38: Connect to Pi
After we have set up the network of Raspberry Pi, we can connect that Pi by SSH or VNC without using TTL cable.
We recommend you using SSH.
Mac OS/Linux users use terminal and Windows users need install SSH client
SSH clients on Windows
  Putty
  OpenSSH (Win10 can enable it)

## Slide 39: Connect to Pi (SSH)
Before using SSH to login Pi, we have to enable SSH of Pi first.
Type
sudo raspi-config

## Slide 40: Connect to Pi (SSH)
Select p2 SSH

## Slide 41: Connect to Pi (SSH)
Enable SSH

## Slide 42: Connect to Pi (SSH)
Putty
Then, we open Putty to connect Pi by SSH.

## Slide 43: Connect to Pi (SSH)
Putty

## Slide 44: Connect to Pi (SSH)
Mac OS terminal
If we are using Unix-like system, just opening the terminal and typing:
ssh pi@"your_Pi_IP"

## Slide 45: Copy file to Pi (SCP)
Usually, we write the code on our own computer and then transfer the source code file to Raspberry Pi.
  To transfer files between a local host and a remote host, we can use Secure copy protocol(SCP).
  SCP has installed in Unix system(command scp). If you have installed OpenSSH in Windows, you
can use scp command in CMD. Otherwise, you can use WinSCP.

## Slide 46: SCP
Windows
Download WinSCP
https://winscp.net/eng/download.php
Host name = IP address
User name = pi
Password = raspberry

## Slide 47: FileZilla
Mac
Download FileZilla
https://filezilla-project.org
Host name = IP address
User name = pi
Password = raspberry
Port = 22
IP address
pi
raspberry
22

## Slide 48: SCP
Linux / Mac OS
Open the terminal and type:
scp filename username@"your_Pi_IP":target_directory
Note that test.txt is in the current directory, you can copy the file in other directory by assigning the full filepath.

## Slide 49: Python & Sensors

## Slide 50: Outline
Python
  Introduction
  Rules
  First Python programming
Sensors
  Introduction
  Digital sensors
  Analog sensors

## Slide 51: Python
Introduction
Interpreted high-level programming language
Compiled language
Source code
Interpreter
processing
Source code
Compiler
preprocessing
machine code
Machine

## Slide 52: Python
Introduction
Dynamically language
  No default types
  a = 1 b = "Hello world"
Strongly typed language
  Stricter typing rules at compile time
  # String + Integer v = " result = " + 100 (wrong)

## Slide 53: Python
Some rules
Python uses indentation to identify coding block.
EX: compare with java
We usually use 4 spaces as indentation.
  Not to use Tab.
JAVA | Python
while (i <= 100) { s += i; i += 1; } | while i <= 100: s += i i += 1

## Slide 54: Python
How to run the first Python programming
In general, there are two ways to run Python.
  Python shell (IDLE)
  Python file

## Slide 55: Python
How to run the first Python programming
Python shell (IDLE)

## Slide 56: Python
How to run the first Python programming
Python file
  Use terminal mode to write code!
Steps
  nano hello.py (create a file hello.py)
  Write code!
  Ctrl+O (save the file), Ctrl+X (leave edit mode)

## Slide 57: Python
How to run the first Python programming
if, if/else, if/elif/else
a = int(input("enter age => "))
if a < 13: print("children") elif a <20:
print("teenager") else: print("adults")

## Slide 58: Python
How to run the first Python programming
for
for i in range(5): print("range(5) value =" + str(i))
while
m = int(input("calculate m!")
r=1
n=1
while n <= m:
r = r * n
n = n + 1
print("m!= " + str(r) )

## Slide 59
Introduction
Sensors
4

## Slide 60
Introduction
Datasheet
5
https://cdn-shop.adafruit.com/datasheets/1899_HTU21D.pdf

## Slide 61
Introduction
Digital & Analog
6
http://www.droneuplift.com/is-ppm-analog-or-digital/

## Slide 62: Introduction
GPIO
7
Board
BCM
Board

## Slide 63
Introduction
Breadboard
8
https://kknews.cc/news/pqprzqj.html

## Slide 64: Digital sensors
LED
Light-emitting diode (LED)
Features
  Efficiency
  Long lifetime
  Cool light
  …
10
GND
Vcc

## Slide 65
Digital sensors
LED
11
https://pimylifeup.com/raspberry-pi-gpio/

## Slide 66
Digital sensors
LED_python
12

## Slide 67: Digital sensors
LED_python
Where is the code?
  Use editor (nano,vi,vim… ) write by yourself
  Use SCP to transfer from your laptop
Run the sample code
  python led_on.py
13

## Slide 68
Digital sensors
LED_Node-RED
14

## Slide 69: Digital sensors
LED advanced
15
https://social.technet.microsoft.com/wiki/contents/articles/34211.c-traffic-lights- simulation-via-leds-on-raspberry-pi.aspx

## Slide 70: Digital sensors
LED advanced
16
python traffic_light.py

## Slide 71
Digital sensors
Push button
17
http://www.ladyada.net/learn/arduino/lesson5.html

## Slide 72
Digital sensors
Push button
18
https://www.sitepoint.com/powering-raspberry-pi-projects-with-php/

## Slide 73: Digital sensors
Push button
19
python push_button_cont rol_led.py

## Slide 74
Digital sensors
Tilt switch
20
http://www.learningaboutelectronics.com/Articles/Tilt-sensor-circuit.php

## Slide 75
Digital sensors
Tilt switch
21
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 76: Digital sensors
Tilt switch
22
python tilt_switch.py

## Slide 77: Digital sensors
23
Buzzer
Self drive buzzer
External drive buzzer
http://www.buzzer-speaker.com/faq/buzzer%20self-external.htm

## Slide 78
Digital sensors
Buzzer
24
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 79: Digital sensors
Buzzer
25
python buzzer.py

## Slide 80
Digital sensors
Piano buzzer
26
https://en.wikipedia.org/wiki/Piano_key_frequencies

## Slide 81
Digital sensors
Piano buzzer
27
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 82
Digital sensors
Piano buzzer
28

## Slide 83
Digital sensors
Piano buzzer
29
python piano_buzzer.py

## Slide 84
Digital sensors
Pyroelectric InfraRed sensor (PIR)
30
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 85
Digital sensors
Pyroelectric InfraRed sensor (PIR)
31
https://learn.adafruit.com/pir-passive-infrared-proximity-motion-sensor/

## Slide 86: Digital sensors
Pyroelectric InfraRed sensor (PIR)
Sensitivity range: up to 20 feet (6 meters) 110° x 70° detection range
Delay time range: 2.45s ~ 248s
Sensitivity range: 3m ~ 7m
Blockade time(Ti): 2.4s
32
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 87
Digital sensors
Pyroelectric InfraRed sensor (PIR)
33
https://learn.adafruit.com/pir-passive-infrared-proximity-motion-sensor/

## Slide 88
Digital sensors
Pyroelectric InfraRed sensor (PIR)
34
python people_alarm_system.py

## Slide 89
Digital sensors
Distance sensor (HC-SR04)
35
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 90: Digital sensors
Distance sensor (HC-SR04)
36
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit
Speed vs. Distance
Resistance

## Slide 91
Digital sensors
Distance sensor (HC-SR04)
37
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 92
Digital sensors
Distance sensor (HC-SR04)
38
python hc_sr04_measure_distance.py

## Slide 93: Analog sensors
40
Photoresistor (light sensor)
Raspberry pi → GPIO inputs are purely digital
MCP3008
  SPI protocol
  10 bits

## Slide 94: Analog sensors
41
Photoresistor (light sensor)
SPI
https://learn.sparkfun.com/tutorials/serial-peripheral-interface-spi

## Slide 95: Analog sensors
42
Photoresistor (light sensor)
Turn on SPI
  sudo raspi-config

## Slide 96: Analog sensors
43
Photoresistor (light sensor)
Check SPI module
Install packages
  sudo apt-get update
  sudo apt-get install –y python-dev python-pip
  sudo pip install spidev

## Slide 97
Analog sensors
Photoresistor (light sensor)
44
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit

## Slide 98: Analog sensors
Photoresistor (light sensor)
45
python photoresistor.py

## Slide 99: Analog sensors
46
Photoresistor (light sensor)
spi.xfer2()
Input (3 bytes)
  Byte 1: the start bit (0x01)
  Byte 2: configure bits
  Byte 3: don’t care
https://www.slideshare.net/raspberrypi-tw/gpio-gameconsolestarterkit